## Slide 1: LISP RLOC GW selection by EEM EID tagging
Toby Rees 30-4-2014

## Slide 2: Problem statement
AT&T need to have simultaneous use of dynamic EID registration via IGP population of XTR database mapping, and EID tagging per RLOC to influence the entry LMGW to the LISP domain.
Dynamic EID requires the use of a single site with the default prefix, allow more specific limiting all registrations to a single route tag.
LMGW selection per RLOC, requires individual tags configured per EID (associated with an RLOC), which negates the option for dynamic IGP based registration.

## Slide 3: Proposed solution
Cisco propose the use of an EEM script running on the MSMR to monitor dynamic registrations and add static mappings for each new EID prefix identified.
These EIDs will be configured using tags derived from community values received from the XTR or Partner.
Use of the EEM script for a given VPN will be controlled by a description of the site 0 location
Each VPN will have a default site defined, with the “accept all” EID definition and a specific route tag. This will be used to register any prefix needed by the customer.

## Slide 4: For Traffic From AGN CALA to TAM (for Stage 1 of Routing Enhancement)
Set CV values for gateway selection (same as in Routing Enhancement Stage 3)
  CV1 => Gateway A, B then C
  CV2 => Gateway B, A then A
  CVx => … Etc.
CE (xTR) advertises RLOC with CVx in LISP Transport VRF
CE (xTR) registers EID with RLOC in MSMR
Configure MSMR with default route 0.0.0.0/0 and allow more specific (with tag 999, for example)
Create EEM script to run on MSMR, periodically (frequency TBD)
  Checking for specific EID registration under the default route (or check for specific tag value such as 999)
  Once specific prefix is found, EEM script needs to use the EID prefix to find the associated RLOC in LISP mapping table on MSMR
  EEM script then uses the RLOC to find the associated CVx that is advertised with this RLOC in LISP Transport VRF
  EEM updates the MSMR configuration tag setting per CVx
MSMR passes the tag to LMGW for Local Pref setting

## Slide 5: From LISP Domain to BGP in AGN
AGN
Network
Partner
Network
(LISP Domain)
MapServer
MapResolver1..n
LMGW1
LMGWn
Advertise RLOC (LB) with CVx in BGP
.
.
.
.
LISP
CE
LAN
WAN
PE
LB
Register EID (LAN) with RLOC (LB) in LISP
LISP Transport VRF
Dest
Next-Hop
PE
LB
CV
CVx
EEM to retrieve CV value and set tag in MSMR
Use Tag to define CV to send to LMGW
LMGW set LP on AGN customer VRF
ASBR1
ASBRn

## Slide 6: Workflow 1 – ssearch (lisp_get_process)
MSMR#show run | inc router lisp
router lisp 1
router lisp 2
MSMR#
Scrape config for lisp processes
LISP process numbers
Find configured LISP process numbers
Record process numbers configured – we need to iterate through.

## Slide 7: Workflow 2 – ssearch (lisp_eem_managed)
Determine if LISP process is EEM script managed
Look for description – if OK continue, else move to next LISP process ID
MSMR#show lisp 1 site name 0000
Site name: 0000
Description: EEM-managed
Allowed configured locators: any
Allowed EID-prefixes:
.
.
.
Show process number site name 0000
Look for description

## Slide 8: Workflow 3a – ssearch (lisp_get_transport_vrf)
For current lisp process MSMR configured for EEM script use.
Record the LISP Transport VRF
MSMR#show lisp 1
Router-lisp ID: 1
Locator table: vrf cust1-rloc
EID instance count: 2
MSMR#
LISP process ID
LISP Transport (RLOC) VRF

## Slide 9: Workflow 3b (If we need to define a new site. TBD) - ssearch (lisp_get_AuthKey_EIDvrf_InstanceID)
For current lisp process MSMR configured for EEM script use.
Record the LISP Transport VRF and authentication key.
router lisp 1
locator-table vrf cust1-rloc
eid-table vrf cust1-eid instance-id 101
ipv4 route-export site-registration
ipv6 route-export site-registration
exit
!
site 0000
description EEM-managed
authentication-key vpn-1-key
eid-prefix instance-id 101 0.0.0.0/0 route-tag 999 accept-more-specifics
eid-prefix instance-id 101 ::/0 route-tag 999 accept-more-specifics
exit
!
!
ipv4 map-server
ipv4 map-resolver
ipv6 map-server
ipv6 map-resolver
exit
LISP process ID
LISP Transport (RLOC) VRF
LISP Instance ID
LISP VPN (EID) VRF
LISP Default site
EEM control description (must match to managed by EEM script)
LISP match all default statements for IPv4 and IPv6
Shared key for VPN

## Slide 10: Workflow 4 – Look for registered prefixes to iterate through - ssearch (lisp_verify_registered_prefixes)
CE XTR registers EID on MSMR. MSMR marks with “default” tag.
Record the EID Prefix, Instance ID and who registered. Ignore the defaults
MSMR#sh lisp 1 site
LISP Site Registration Information
Site Name Last Up Who Last Inst EID Prefix
Register Registered ID
0000 never no -- 101 0.0.0.0/0
00:00:56 yes 172.16.1.2 101 172.16.100.3/32
Show command for LISP process 1 prefixes
LISP Instance ID
Default prefix (unregistered)
LISP Default site
Registered prefix RLOC
Dynamic registered prefix

## Slide 11: Workflow 5 – Examine a prefix - ssearch (lisp_examine_prefix)
Identify that this prefix is being learned by the dynamic match using either the default tag or the Dynamic origin line.
Record the ETR address (may be different from the RLOC seen previously)
MSMR#show lisp 1 site 172.16.100.3/32 instance-id 101
LISP Site Registration Information
Site name: 0000
Description: EEM-managed
Allowed configured locators: any
Requested EID-prefix:
EID-prefix: 172.16.100.3/32 instance-id 101
First registered: 02:15:34
Routing table tag: 999
Origin: Dynamic, more specific of 0.0.0.0/0
Merge active: No
Proxy reply: No
TTL: 1d00h
State: complete
Registration errors:
Authentication failures: 0
Allowed locators mismatch: 0
ETR 172.16.1.2, last registered 00:00:15, no proxy-reply, map-notify
TTL 1d00h, no merge, hash-function sha1, nonce 0xCA9A607C-0x0E974520
state complete, no security-capability
xTR-ID 0xFE78594D-0x51D6BCB2-0xE0A7FBE9-0x28CFC0AB
site-ID unspecified
Locator Local State Pri/Wgt Scope
172.12.12.1 yes up 1/1 IPv4 none
MSMR#
For each prefix in this process
Verify this is registered as dynamic with route Tag
Locator Address
ETR Address

## Slide 12: Workflow 6 – find a community value - ssearch (lisp_get_community)
If not already identified (from previous prefix) Look for Community value associated with Locator address of EID in Transport (RLOC) VRF defined in config.
Record the community value.(Will be one of a few possible)
MSMR#sh ip bgp vpnv4 vrf cust1-rloc 172.12.12.1
BGP routing table entry for 991:1:172.12.12.1/32, version 214
Paths: (1 available, best #1, table cust1-rloc)
Advertised to update-groups:
15
Refresh Epoch 1
65001 2 500 65001
10.10.1.2 (via vrf cust1-rloc) from 10.10.1.2 (10.200.200.1)
Origin IGP, localpref 100, valid, external, best
Community: 90
mpls labels in/out 29/nolabel
rx pathid: 0, tx pathid: 0x0
MSMR#
For each prefix in this process
Verify this is registered as dynamic with route Tag

## Slide 13: Workflow 7 – Define new EID - ssearch (LISP_DefineEID.tcl)
Using previously recorded information add new EID definition.
MSMR#conf t
Enter configuration commands, one per line. End with CNTL/Z.
MSMR(config)#router lisp 1
MSMR(config-router-lisp)#site 0000
MSMR(config-router-lisp-site)#eid-prefix instance-id 101 172.16.100.3/32 route-tag 90
MSMR(config-router-lisp-site)#
Instance ID recorded in step 4
Current LISP process from step 1
Default Site ID (may change to denote Dynamic ID site)
EID prefix recorded in step 4
Community value recorded in step 6

## Slide 14: Possible Enhancements
Add CLI to show all LISP processes in one command. Same as show lisp 1 site.
  show lisp * site
Add CLI to show tag associated with EID registration. Includes eid, IID, RLOC and tag.
  Show lisp * site tag
Add CLI to show RLOC VRF associated with LISP process
  Show lisp * site tag rloc_vrf
If possible it would be awesome to have all the options available at once so we could parse the whole lot in one go. So on one line the output would be
Process, IID, EID, RLOC , tag, VRF.
  Show lisp * site tag rloc_vrf