## Slide 1: vRR Backup Router EEM Scripts
Gowtham Tamilselvan and Jason Froehlich
Cisco Advanced Services
September 4, 2019

## Slide 2: Agenda
vRR EEM Scripts Introduction
    Detection Script
    Remediation Script
    Recovery Script
vRR EEM Scripts Requirements
vRR EEM Deployment Guidelines
vRR EEM Base Configuration
    Intra-AS vRRb BGP Config
    vSABR vRRb BGP config
Demo
Syslog Captures

## Slide 3: vRR EEM Scripts Introduction

## Slide 4: 3 Script Approach
1:N backup router concept
Detection Script
  Backup Router will be monitoring the active vRRs to detect failure condition
Remediation Script
  Once the backup router detects failure of an active vRR, it will load the config needed to become that active vRR
Recovery Script
  The backup router will monitor for the active vRR to come back up, and will revert to backup role once the active is back up.

## Slide 5: Phase 1 – Detection/Monitoring
Triggered based on the bgp session state change between the vRRb and active vRRs
iBGP session between the two routers based on non-zero loop IP
Once invoked the detection script will go through a set of checks to determine if the active router is indeed down.
If detection script confirms failure of active router, it will then invoke the remediation script (phase 2)

## Slide 6: Detection Script Checks
Triggered on BGP session going down between vRRb and an active vRR
    iBGP session using a new loopback ID (non-zero)
Ping checks from vRRb and the active vRR
    Detection script will check reachability of the active vRR’s loopback 0 IP address
    Detection script will check reachability of the active vRR’s MGMT IP address
RIB Route checks from vRRb and the active vRR
    Detection script will check the RIB for the active vRR’s loopback 0 IP address
Ping checks from vRRb and the CBB core routers
    Detection script will check reachability of the backup router to other CBB routers, to ensure the fault is not on the backup router. (Ensure backup router is not isolated)
If all checks indicate a failure condition on the active vRR, then the backup router will register and trigger the remediation script.
vRRb router is now ready to take over the primary role and become the active vRR that went down.

## Slide 7: Phase 2 – Remediation
IGP should be up for vRRb as part of base config (not part of EEM)
vRRb will need to contain the BGP neighbor-groups for each vPE configured and in-shut down state.
There will be 5 different active router’s config on disk0 of vRRb router
The remediation script will load and commit the config file that corresponds to active router which failed as confirmed by the detection script
The loaded config file will contain the neighbor which needs to unshut, and the loopback configuration for the vRRb router to mimic the active failing vRR
Once vRRb is actively participating in production network, prior EEM detection script will be unregistered so it does not get triggered again.
The remediation script will invoke Recovery EEM script after configuration and post checks are done

## Slide 8: Remediation Script Checks
Triggered on syslog message printed by the detection script
    Specific syslog message that will pass required variables from detection script to remediation script
    +++++EEM policy vrr_remediation_script for node RR248 config_file_location disk0:/eem/configs/RR248_bgp_cfg vRR_MGMT_IP 1.3.249.248 vRR_Loop_IP 12.122.249.248 vRR_BGP_IP 12.122.250.248 start now!!+++++
Remediation script will unregister the detection script
Load and commit the config file for the failing-active-router (determined by syslog trigger)
    If there is a load or commit failure then the remediation script will exit and send an alert for manual intervention
At this point the backup router has become an active router, participating in the network
Ping checks from vRRb and CBB core routers with the source of new loopback
    Remediation script will check reachability of the backup vRR (now active) using the new loopback IP address
    New loopback IP address will be the same as the loopback 0 IP address of the failed-active-vRR
BGP Session checks from vRRb and the Pes (of failed-active-vRR)
    If more than 50% of the BGP sessions are down then script will wait and recheck the sessions
Lastly the Remediation script will register the Recovery script (Phase 3)
Notes: RP/0/RP0/CPU0:Aug 30 22:55:50.357 UTC: tclsh[68145]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: +++++EEM policy vrr_remediation_script for node RR248 config_file_location disk0:/eem/configs/RR248_bgp_cfg vRR_MGMT_IP 1.3.249.248 vRR_Loop_IP 12.122.249.248 vRR_BGP_IP 12.122.250.248 start now!!+++++

## Slide 9: Phase 3 – Recovery
vRRb router is now an active RR participating in the network
Once the previously failed-active-vRR starts to recover and come back online, we will need the backup router to relinquish the active role and revert back the backup role
Recovery script will apply the configuration changed needed to move the vRRb router back to the backup role
A “recovery-cleanup-cfg” file must be present in vRRb disk and contain the configs needed to revert back
    Configs to shutdown the active-vRR’s neighbor-group and loopback config
Once recovery script performs the config changes and post-checks it will register the detection script and unregister itself
Notes: Or EEM script to ping Mgmt Eth0 of prior active vRR if IPSLA is not available
If it is reachable, then shut down the loopback and neighbor group on vRRb, and revert to old loop ip and peer with production vRR.
Invoke the detection EEM script

## Slide 10: Recovery Script Checks
Triggered on BGP session coming up between the vRRb (now active) and failed-active-router (that has now recovered from failure condition)
    Same iBGP session using a loopback ID (non-zero) used in detection script
    BGP session coming up indicates the failed router has recovered
Recovery script will ping the failed-active-vRR’s MGMT interface to ensure that this router is up
Recovery script will then unregister the remediation script and prepare for config changes
Recovery script will load and commit the recovery-cleanup-cfg file
    If there is a load or commit failure then the recovery script will shutdown its uplinks (to isolate itself) and send an alert for manual intervention
    Safer for vRRb to isolated than to have a split-brain condition with Pes seeing two active vRRs
If load and commit are successful, then the vRRb router has become the backup router again
RIB route check performed to ensure the active-vRR’s loopback 0 is seen
Ping checks from vRRb and active-vRR’s loopback 0 IP address
The Recovery script will register the Detection script (Phase 1) again and unregister itself (coming full circle)
Notes: RP/0/RP0/CPU0:Aug 30 22:55:50.357 UTC: tclsh[68145]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: +++++EEM policy vrr_remediation_script for node RR248 config_file_location disk0:/eem/configs/RR248_bgp_cfg vRR_MGMT_IP 1.3.249.248 vRR_Loop_IP 12.122.249.248 vRR_BGP_IP 12.122.250.248 start now!!+++++

## Slide 11: vRR EEM Script Requirements

## Slide 12: Detection Script Requirements
Trigger Pattern
      ::cisco::eem::event_register_syslog pattern "ROUTING-BGP-5-ADJCHANGE.*neighbor.*Down.*VRF: default.*AS: 13979.*" maxrun 750
Require following default variables to be edited manually by AT&T for all 5 active vRRs monitored by the backup vRR
      set activeRR1 [ list loop0_ip nodename mgmt_ip loop250_ip configfilelocation sleeptimer]
      Example: set activeRR1 [list 12.122.249.245 RR245 1.3.249.245 12.122.250.245 $_config_storage_location/RR245_bgp_cfg 10]
Requires a list of CBB Routers reachable by the vRR
      set cbb_ip [ list cbbloopbackip1 cbbloopbackip2 ...]
      Example: set cbb_ip [list 12.122.0.7 12.122.0.4]
Require the vRR_detection_logs directory to be present under disk0:/eem/
Creates a vrr-detection-active file on disk0:/eem/ which is used to prevent multiple iterations of detection script being run/triggered.

## Slide 13: Remediation Script Requirements
Trigger Pattern
      ::cisco::eem::event_register_syslog pattern "HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO.*EEM policy vrr_remediation_script.*node.*config_file_location.*vRR_MGMT_IP.*vRR_Loop_IP.*start.*" maxrun 750
Requires a list of CBB Routers reachable by the vRR
      # set cbb_ip [ list cbbloopbackip1 cbbloopbackip2 ...]
      set cbb_ip [list 12.122.0.7 12.122.0.4]
Requires a sleeptimer variable to be set
      Set sleeptime <value in seconds>
      Example: set sleeptimer 30
Require the vRR_remediation_logs directory to be present under disk0:/eem/
Creates a file called vrr-remediation-active which is used to pass variable information from remediation script to recovery script.
Notes: Detection script will print the following syslog message which will then trigger the remediation script.
RP/0/RP0/CPU0:Aug 30 21:09:12.527 UTC: tclsh[68900]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: +++++EEM policy vrr_remediation_script for node RR251 config_file_location disk0:/eem/configs/RR251_bgp_cfg vRR_MGMT_IP 1.3.249.251 vRR_Loop_IP 12.122.249.251 vRR_BGP_IP 12.122.250.251 start now!!+++++

## Slide 14: Recovery Script Requirements
Trigger Pattern
      ::cisco::eem::event_register_syslog pattern "ROUTING-BGP-5-ADJCHANGE.*neighbor.*Up.*VRF: default.*AS: 13979.*" maxrun 600
Requires the file location and name of the recovery file to be defined
      set recoveryfile <disk0:/eem/configs/recoverycleanupfilename>
      Default value: set recoveryfile "disk0:/eem/configs/recovery_cleanup_cfg”
Requires a sleeptimer variable to be set
      Set sleeptime <value in seconds>
      Example: set sleeptimer 30
Requires the disk0:/eem/vrr-remediation-active file to be present (this file is created by remediation script)
Requires the vRR_recovery_logs directory to be present under disk0:/eem/
Creates a file called vrr-recovery-active which is used to prevent multiple iterations of recovery script being run/triggered
Upon successful completion of recovery script, it will delete all the vrr-*-active files in disk0:/eem/
Notes: Recovery script will also create a file called vrr-recovery-active to prevent multiple iterations of recovery script getting triggered. But the recovery script will delete this file as well as the other vrr-*-active files after successful completion.

## Slide 15: vRR EEM Deployment Guidelines

## Slide 16: vRRb Deployment Model
One vRRb acts as backup to ~5 Active vRR
  Exclusive backup role – first to fail
Active vRR pool exists within single Plane (different Regions)
  Unique/non-overlapping Clients
  Uniform set of Non-clients

## Slide 17: EEM Script Deployment Overview
Apply updated config on Active vRR’s
Apply Base config on vRRb
Customize variables in script files
Prepare directories, copy script and config files
Apply EEM environment config
Register Detection script

## Slide 18: Active vRR Config Changes
New Loopback100 used for keepalive to vRRb
  Advertised into OSPF
BGP Neighbor to vRRb
  Sourced from new Loopback100
  IPv4 Unicast address-family only
interface Loopback100
description BGP Peering to Backup VRR
ipv4 address $ip_address
!
router ospf 2
area 10.10.34.9
interface Loopback100
cost 10000
!
router bgp 13979
neighbor 12.122.249.249
remote-as 13979
update-source Loopback100
address-family ipv4 unicast
route-policy BRICKWALL in
route-policy BRICKWALL out
!

## Slide 19: Base Config for vRRb
Global configuration matching standard vRR templates
  Admin, Syslog, AAA, NTP, ACL, etc.
Slightly modified OSPF and BGP configurations
Configs discussed in next sections
  Based on “IOS XR RR CCR Version 3.8”

## Slide 20: Edit “vrr_syslog_detection.tcl” Script File
Lines 90-99
  Create list entry for each Active-vRR being protected
  set activeRR<1-5> [list <vRR_Loop0> <vRR_Name> <vRR_MgmtEth> <vRR_Loop100> $_config_storage_location/<vRR_config_file> <sleep_timer>]
  Ex: set activeRR1 [list 12.122.249.245 RR245 1.3.249.245 12.122.250.245 $_config_storage_location/RR245_bgp_cfg 30]
Line 101
  Specify Loop0 IP addresses of two CBB Core nodes
  Used to confirm vRRb’s reachability to network
  set cbb_ip [list <core_ip_1> <core_ip_2>]
  Ex: set cbb_ip [list 12.122.0.7 12.122.0.4]

## Slide 21: Edit “vrr_syslog_remediation.tcl” Script File
Line 64
  Specify Loop0 IP addresses of two CBB Core nodes
  Used to confirm vRRb’s reachability to network
  set cbb_ip [list <core_ip_1> <core_ip_2>]
  Ex: set cbb_ip [list 12.122.0.7 12.122.0.4]
Line 65
  Specify sleep timer value, used as delay to prevent false positives
  set sleeptimer <seconds>
  Ex: set sleeptimer 30

## Slide 22: Edit “vrr_syslog_recovery.tcl” Script File
Line 65
  Specify cleanup file location
  set recoveryfile "disk0:/eem/configs/<cleanup_file>"
  Ex: set recoveryfile "disk0:/eem/configs/recovery_cleanup_cfg"
Line 67
  Specify sleep timer value, used as delay to prevent false positives
  set sleeptimer <seconds>
  Ex: set sleeptimer 30

## Slide 23: Prepare Disk Location (Shell)
Enter shell
  run
Create Directories
  mkdir /disk0/eem
  mkdir /disk0/eem/configs
  mkdir /disk0/eem/vRR_recovery_logs
  mkdir /disk0/eem/vRR_detection_logs
  mkdir /disk0/eem/vRR_remediation_logs

## Slide 24: EEM AAA Configuration (Config Mode)
Add EEM User
  username eem-user
  group root-lr
  group cisco-support
Add AAA groups
  aaa authorization exec eem-user local
  aaa authorization commands eem-user none
  aaa authorization eventmanager eem-user local
  aaa authentication login eem-user local

## Slide 25: EEM Process and Line Configuration (Config Mode)
Specify directory for EEM scripts
  event manager directory user policy disk0:/eem
Create and enable line pool for EEM
  line template EEM
  authorization exec eem-user
  authorization commands eem-user
  !
  vty-pool eem 100 105 line-template EEM

## Slide 26: EEM Environment Configuration (Config Mode)
Specify E-mail server details
  event manager environment _email_to $dest_mailer_address
  event manager environment _domainname $domain_name
  event manager environment _email_from $source_email_address
  event manager environment _email_server $ip_address
Specify location of config and log files
  event manager environment _eem_storage_location disk0:/eem
  event manager environment _config_storage_location disk0:/eem/configs
  event manager environment _recovery_storage_location disk0:/eem/vRR_recovery_logs
  event manager environment _detection_storage_location disk0:/eem/vRR_detection_logs
  event manager environment _remediation_storage_location disk0:/eem/vRR_remediation_logs

## Slide 27: Copy/Create EEM Script Files
Exec Mode
  copy ftp://$user@$server//$path/vrr_syslog_detection.tcl disk0:/eem/vrr_syslog_detection.tcl
  copy ftp://$user@$server//$path/vrr_syslog_remediation.tcl disk0:/eem/vrr_syslog_remediation.tcl
  copy ftp://$user@$server//$path/vrr_syslog_recovery.tcl disk0:/eem/vrr_syslog_recovery.tcl
-or-
Shell
  nano /disk0:/eem/vrr_syslog_detection.tcl
  nano /disk0:/eem/vrr_syslog_remediation.tcl
  nano /disk0:/eem/vrr_syslog_recovery.tcl

## Slide 28: Copy/Create Active-vRR Config and Cleanup Files
Exec Mode
  copy ftp://$user@$server//$path/Active_vRR1_cfg disk0:/eem/configs/Active_vRR1_cfg
  copy ftp://$user@$server//$path/Active_vRR2_cfg disk0:/eem/configs/Active_vRR2_cfg
  ...
  copy ftp://$user@$server//$path/recovery_cleanup_cfg disk0:/eem/configs/recovery_cleanup_cfg
Shell
  nano /disk0:/eem/configs/Active_vRR1_cfg
  nano /disk0:/eem/configs/Active_vRR2_cfg
  ...
  nano /disk0:/eem/configs/recovery_cleanup_cfg

## Slide 29: Activate Detection EEM Script (Config Mode)
Register vrr_detection_script.tcl script
  event manager policy vrr_detection_script.tcl username eem-user persist-time 3600
Unregister vrr_detection_script.tcl script with no command
  no event manager policy vrr_detection_script.tcl username eem-user persist-time 3600
  Unregistering the policy will terminate any active threads

## Slide 30: Verify Script is Activated
Show event manager policy registered
  RP/0/RP0/CPU0:RR249-VRR#show event manager policy registered
  Tue Sep 3 23:37:56.539 UTC
  No. Class Type Event Type Trap Time Registered Name
  1 script user syslog Off Fri Aug 30 21:01:51 2019 vrr_detection_script.tcl
  pattern {ROUTING-BGP-5-ADJCHANGE.*neighbor.*Down.*VRF: default.*AS: 13979.*}
  nice 0 queue-priority normal maxrun 750.000 scheduler rp_primary Secu none
  persist_time: 3600 seconds, username: eem-user

## Slide 31: vRRb Base Configuration

## Slide 32: vRRb Base Config– Loopback Interfaces
Loopback 0
  Used as OSPF and BGP Router ID
  Used for Keepalive BGP peering to Active vRRs
Loopback 100
  Used for BGP peering to Active vRR’s clients/non-clients
  Assumes IP address of Active vRR’s Loopback 0
  Remains in Shutdown state with no IP until vRRb takes over Active role
  Description and IP address changed by script upon takeover
interface Loopback0
ipv4 address $ip_address
interface Loopback100
description Active vRR Loopback0
shutdown

## Slide 33: vRRb Base Config - OSPF
Standard vRR OSPF process config
Add Loopback 100 with cost of 20000
  Higher cost will ensure BGP clients prefer the real Active vRR once it recovers
router ospf 2
log adjacency changes
router-id $loopback0_address
timers throttle spf 150 150 5000
spf prefix-priority route-policy ospf-spf-priority
area 10.10.34.9
network point-to-point
interface Loopback0
!
interface Loopback100
cost 20000
!
interface GigabitEthernet0/0/0/0
cost 10000
!
interface GigabitEthernet0/0/0/1
cost 10000
!
!
!

## Slide 34: vRRb Base Config – BGP Keepalive Neighbors
BGP Neighbor to each Active vRR’s Loopback 100 for failure detection
Only IPv4 Unicast address-family used
Sourced from vRRb’s Loopback0
Faster timers may be used for quicker failure detection
router bgp 13979
neighbor 12.122.250.245
remote-as 13979
description vRRb Keepalive to $active_vrr
update-source Loopback0
address-family ipv4 unicast
route-policy BRICKWALL in
route-policy BRICKWALL out
!
!

## Slide 35: Intra-AS vRRb BGP Config

## Slide 36: vRRb Base Config – BGP (Intra-AS)
Standard Intra-AS vRR BGP process config
Cluster-ID remains unconfigured
  Will be configured by script based on Active RR role
address-family ipv4 unicast
update limit address-family 5
!
address-family vpnv4 unicast
update limit address-family 175
update limit sub-group ebgp 10
update limit sub-group ibgp 25
!
address-family vpnv6 unicast
update limit address-family 10
!
address-family ipv4 mdt
update limit address-family 5
!
address-family l2vpn vpls-vpws
update limit address-family 50
update limit sub-group ebgp 10
update limit sub-group ibgp 25
!
address-family ipv4 rt-filter
update limit address-family 5
!
address-family vpnv6 multicast
update limit address-family 5
router bgp 13979
bgp router-id $loopback0_address
no bgp cluster-id
bgp update-delay 360
update limit 200
!

## Slide 37: vRRb Base Config – BGP Groups and RPL (Intra-AS)
Community Sets
  All documented in CCR
Route Policies
  All documented in CCR
BGP AF-Groups
  All documented in CCR
BGP Session Groups
  All modified from CCR (see next slides)
BGP Neighbor Groups
  All documented in CCR
  Except: (see next slides)
    MIPE_CLUSTER_IBGP_RR_2_PE
    RR_2_VPLS_PE
    RR_2_AIC_LEAF_ROUTER
    AVPN_IBGP_RR_2_IPE

## Slide 38: vRRb Base Config – BGP Session Groups (Intra-AS)
Modify BGP Session groups to use the Loopback100 source interface
router bgp 13979
session-group 7018_IBGP
remote-as 7018
advertisement-interval 0
local-as 7018 no-prepend
update-source Loopback100
!
session-group 13979_IBGP
remote-as 13979
advertisement-interval 0
update-source Loopback100
!
session-group 20057_IBGP
remote-as 20057
advertisement-interval 0
local-as 7018 no-prepend
update-source Loopback100

## Slide 39: vRRb Base Config – BGP Neighbor Groups (Intra-AS)
BGP neighbor groups used to activate client BGP sessions when vRRb becomes active.
All neighbor groups start in the SHUTDOWN state
Each Active vRR has its own set of neighbor groups on the vRRb; clients are preconfigured to use the respective neighbor groups
  Based on Region (NE1, NE2, NC1, NC2, NW, SE, SC, SW)
neighbor-group SC_CLUSTER_IBGP_RR_2_PE
use session-group 13979_IBGP
shutdown
…

## Slide 40: vRRb Base Config – BGP Neighbor Groups (Intra-AS)
New BGP Neighbor Groups required to differentiate these Active vRR clients:
    MIPE_CLUSTER_IBGP_RR_2_PE
    RR_2_VPLS_PE
    RR_2_AIC_LEAF_ROUTER
    AVPN_IBGP_RR_2_IPE
New name: add “_$region” suffix
Contents of each NG are identical
neighbor-group RR_2_AIC_LEAF_ROUTER_NW
use session-group 7018_IBGP
shutdown
address-family ipv4 unicast
use af-group IBGP_IPV4
!
address-family vpnv4 unicast
route-reflector-client
!
address-family vpnv6 unicast
route-reflector-client
!
address-family ipv4 rt-filter
use af-group IBGP_RR_2_PE_RTC
!
!

## Slide 41: vRRb Base Config – BGP Client Neighbors (Intra-AS)
BGP Clients from each Active vRR preconfigured in separate Neighbor Groups
!! Active vRR 1 Clients
neighbor 12.129.0.1
use neighbor-group SW_CLUSTER_IBGP_RR_2_PE
!
neighbor 12.129.0.2
use neighbor-group SW_CLUSTER_IBGP_RR_2_PE
!
!! Active vRR 2 Clients
neighbor 12.129.1.1
use neighbor-group SC_CLUSTER_IBGP_RR_2_PE
!
neighbor 12.129.1.2
use neighbor-group SC_CLUSTER_IBGP_RR_2_PE
!
!! Active vRR 3 Clients
neighbor 12.129.2.1
use neighbor-group SE_CLUSTER_IBGP_RR_2_PE
!
neighbor 12.129.2.2
use neighbor-group SE_CLUSTER_IBGP_RR_2_PE
!

## Slide 42: Active vRR-specific Config File (Intra-AS)
One file per Active vRR
Located in disk0:/eem/configs
Loaded and committed by Phase 2 – Remediation script
!! Apply cluster ID
router bgp 13979
bgp cluster-id 12.122.249.2
!! No-shut client neighbor groups
neighbor-group RR_2_VPLS_PE_NW
no shutdown
neighbor-group AVPN_IBGP_RR_2_IPE_NW
no shutdown
neighbor-group NW_CLUSTER_IBGP_RR_2_PE
no shutdown
neighbor-group RR_2_AIC_LEAF_ROUTER_NW
no shutdown
neighbor-group MIPE_CLUSTER_IBGP_RR_2_PE_NW
no shutdown
!! Load non-client neighbor configs
neighbor 12.122.249.204
use neighbor-group IBGP_RR_2_RR
neighbor 12.122.249.210
use neighbor-group IBGP_RR_2_RR
!! Apply loopback Config
interface Loopback100
description $active-vrr Loopback0
ip address $ip_address
no shutdown

## Slide 43: Generic Config Cleanup File (Intra-AS)
One file for ALL Active vRR’s
Located in disk0:/eem/configs
Name: recovery_cleanup_cfg
Loaded and committed by Phase 3 – Recovery script
!! Remove cluster ID
router bgp 13979
no bgp cluster-id
!! Shut ALL client neighbor groups
neighbor-group RR_2_VPLS_PE_NW
no shutdown
neighbor-group RR_2_VPLS_PE_SE
no shutdown
neighbor-group RR_2_VPLS_PE_SW
no shutdown
...
!! Remove ALL non-client neighbor configs
no neighbor 12.122.249.204
no neighbor 12.122.249.210
...
!! Reset loopback Config
interface Loopback100
description Active-vRR Loopback0
no ip address
shutdown

## Slide 44: Ongoing Operations/Maintenance (Intra-AS)
BGP Client MACD
  New/Old BGP neighbor must be added/removed from appropriate neighbor group in vRRb’s running config
  Expected to be handled by provisioning tools
BGP Non-Client MACD
  New/Old BGP neighbor must be added/removed from the Active-vRR-specific config file and generic cleanup file on vRRb’s disk0:
  Expected to be uncommon
  Must be manually modified

## Slide 45: vSABR vRRb BGP Config

## Slide 46: vRRb Base Config – BGP (vSABR)
Standard vSABR vRR BGP process config
Cluster-ID remains unconfigured
  Will be configured by script based on Active RR role
address-family vpnv6 unicast
update limit address-family 10
!
address-family ipv4 mdt
update limit address-family 5
!
address-family l2vpn vpls-vpws
update limit address-family 50
update limit sub-group ebgp 10
update limit sub-group ibgp 25
!
address-family ipv4 rt-filter
update limit address-family 5
source route-target route-policy STATIC_RTC_LIST_vSABR
!
address-family vpnv6 multicast
update limit address-family 5
!
address-family ipv4 mvpn
address-family ipv6 mvpn
!
address-family l2vpn vpls-vpws
update limit address-family 50
update limit sub-group ebgp 10
update limit sub-group ibgp 25
!
ibgp policy out enforce-modifications
router bgp 13979
bgp router-id $loopback0_address
no bgp cluster-id
bgp update-delay 360
update limit 200
!
address-family ipv4 unicast
update limit address-family 5
!
address-family vpnv4 unicast
update limit address-family 175
update limit sub-group ebgp 10
update limit sub-group ibgp 25
!

## Slide 47: vRRb Base Config – BGP Groups and RPL (vSABR)
Community Sets
  All documented in CCR
Extcommunity Sets
  All documented in CCR
Route Policies
  All documented in CCR
BGP Session Groups
  All modified from CCR (see next slides)
BGP Neighbor Groups
  All documented in CCR

## Slide 48: vRRb Base Config – BGP Session Groups (vSABR)
Modify BGP Session groups to use the Loopback100 source interface
session-group SABR_IBGP
remote-as 13979
advertisement-interval 0
update-source Loopback100
!
session-group SABR_MPEBGP
ebgp-multihop 50
advertisement-interval 0
update-source Loopback100

## Slide 49: vRRb Base Config – BGP Neighbors (vSABR)
vSABR BGP neighbors cannot be preconfigured due to overlap
  A1 West SABR-O peers with same clients as A1 East SABR-O
Must be defined in the Active vRR-specific config file on disk0: and loaded by script
RR
253
Backup

## Slide 50: Active vRR-specific Config File (vSABR)
One file per Active vRR
Located in disk0:/eem/configs
Loaded and committed by Phase 2 – Remediation script
!! Apply cluster ID
router bgp 13979
bgp cluster-id 12.122.249.2
!! Load client neighbor configs
neighbor 12.122.249.204
use neighbor-group SABR_A1_2_PLANE_F_INTRA_AS_RR
neighbor 12.122.249.210
use neighbor-group SABR_A1_2_PLANE_F_INTRA_AS_RR
neighbor 12.122.249.200
use neighbor-group SABR_2_MOBILITY
!! Load non-client neighbor configs
neighbor 12.122.249.224
use neighbor-group SABR_2_SABR
remote-as $ASN
neighbor 12.122.249.230
use neighbor-group SABR_2_SABR
remote-as $ASN
!! Apply loopback Config
interface Loopback100
description $active-vrr Loopback0
ip address $ip_address
no shutdown

## Slide 51: Generic Config Cleanup File (vSABR)
One file for ALL Active vRR’s
Located in disk0:/eem/configs
Name: recovery_cleanup_cfg
Loaded and committed by Phase 3 – Recovery script
!! Remove cluster ID
router bgp 13979
no bgp cluster-id
!! Remove ALL client and non-client neighbor configs
no neighbor 12.122.249.204
no neighbor 12.122.249.210
no neighbor 12.122.249.200
no neighbor 12.122.249.224
no neighbor 12.122.249.230
...
!! Reset loopback Config
interface Loopback100
description Active-vRR Loopback0
no ip address
shutdown

## Slide 52: Ongoing Operations/Maintenance (vSABR)
BGP Client and Non-Client MACD
  New/Old BGP neighbor must be added/removed from the Active-vRR-specific config file and generic cleanup file on vRRb’s disk0:
  Expected to be uncommon
  Must be manually modified

## Slide 53: DEMO

## Slide 54: Syslog Captures

## Slide 55: Detection Script Logs (on failure detection)
RP/0/RP0/CPU0:RR253-VRR#RP/0/RP0/CPU0:Sep 3 23:44:20.494 UTC: bgp[1060]: %ROUTING-BGP-5-ADJCHANGE : neighbor 12.122.250.251 Down - BGP Notification received, hold time expired (VRF: default) (AS: 13979)
RP/0/RP0/CPU0:Sep 4 00:16:23.789 UTC: logger[67101]: %OS-SYSLOG-6-LOG_INFO : %ROUTING-BGP-5-ADJCHANGE : neighbor 12.122.250.251 Down - BGP Notification received, hold time expired (VRF: default) (AS: 13979)
RP/0/RP0/CPU0:RR253-VRR#RP/0/RP0/CPU0:Sep 4 00:16:23.956 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: EEM policy vrr_detection_script.tcl has started
RP/0/RP0/CPU0:Sep 4 00:16:31.030 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for node RR251 - bgp_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:16:33.507 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: EEM policy vrr_detection_script iBGP Status between vRRb and vRR RR251 is in Idle state, script will continue with the checks.
RP/0/RP0/CPU0:Sep 4 00:16:33.508 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for active vRR RR251 on backup vRR RR253 - bgp_check procedure completed------
RP/0/RP0/CPU0:Sep 4 00:16:33.508 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for node RR251 - ping_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:16:47.858 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: EEM policy vrr_detection_script PING to IP 12.122.249.251 of RR251 Failed.
RP/0/RP0/CPU0:Sep 4 00:16:47.859 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for active vRR RR251 on backup vRR RR253 - ping_check procedure for loopback0 completed------
RP/0/RP0/CPU0:Sep 4 00:16:47.860 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for node RR251 - ping_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:17:03.800 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: EEM policy vrr_detection_script PING to IP 1.3.249.251 of RR251 Failed.
RP/0/RP0/CPU0:Sep 4 00:17:03.800 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for active vRR RR251 on backup vRR RR253 - ping_check procedure for MGMT_IP completed------
RP/0/RP0/CPU0:Sep 4 00:17:03.803 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for node RR251 - route_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:17:06.305 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: EEM Dectection Script - RIB Route check for 12.122.249.251 of RR251 Failed, route not found, script will continue with the checks.
RP/0/RP0/CPU0:Sep 4 00:17:06.310 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for active vRR RR251 on backup vRR RR253 - route_check procedure completed------

## Slide 56: Detection Script Logs (on failure detection)
RP/0/RP0/CPU0:Sep 4 00:17:06.310 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for active vRR RR251 on backup vRR RR253 - route_check procedure completed------
RP/0/RP0/CPU0:Sep 4 00:17:06.310 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for node RR251 - ping_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:17:09.054 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: EEM policy vrr_detection_script PING to IP 12.122.0.7 of RR251 successful.
RP/0/RP0/CPU0:Sep 4 00:17:11.880 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: EEM policy vrr_detection_script PING to IP 12.122.0.4 of RR251 successful.
RP/0/RP0/CPU0:Sep 4 00:17:11.881 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for active vRR RR251 on backup vRR RR253 - ping_check procedure for CBB Core Routers completed------
RP/0/RP0/CPU0:Sep 4 00:17:11.882 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: EEM policy vrr_detection_script has detected a Failure for node RR251
RP/0/RP0/CPU0:Sep 4 00:17:11.883 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: Sending Email Alert - EEM vRR Detection for node RR251 to gtamilse@cisco.com
RP/0/RP0/CPU0:Sep 4 00:17:12.081 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for node RR251 - register_remediation procedure started------
RP/0/RP0/CPU0:Sep 4 00:17:17.541 UTC: eem_policy_dir[326]: %HA-HA_EM-6-FMPD_POLICY_REG_SUCC : fh_reg_unreg_policy: Policy 'vrr_remediation_script.tcl' registered successfully, by user eem-user, with persist time 3600 and type 2
RP/0/RP0/CPU0:Sep 4 00:17:18.574 UTC: config[67488]: %MGBL-CONFIG-6-DB_COMMIT : Configuration committed by user 'eem-user'. Use 'show configuration commit changes 1000000886' to view the changes.
RP/0/RP0/CPU0:Sep 4 00:17:18.958 UTC: config[67488]: %MGBL-SYS-5-CONFIG_I : Configured from console by console on vty101 (0.0.0.0)
RP/0/RP0/CPU0:Sep 4 00:17:19.443 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script on backup vRR RR253 - remediation script registeration successful------
RP/0/RP0/CPU0:Sep 4 00:17:19.443 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script on backup vRR RR253- register_remediation procedure completed------
RP/0/RP0/CPU0:Sep 4 00:17:19.444 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_syslog_detection script for node RR251 - disk0:/eem/configs/RR251_bgp_cfg config file exists------
RP/0/RP0/CPU0:Sep 4 00:17:19.445 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: ------EEM policy vrr_detection_script for node RR251 completed!!------
RP/0/RP0/CPU0:Sep 4 00:17:19.446 UTC: tclsh[67107]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_detection_script.tcl: +++++EEM policy vrr_remediation_script for node RR251 config_file_location disk0:/eem/configs/RR251_bgp_cfg vRR_MGMT_IP 1.3.249.251 vRR_Loop_IP 12.122.249.251 vRR_BGP_IP 12.122.250.251 start now!!+++++

## Slide 57: Remediation Script Logs (on vRRb becoming active)
RP/0/RP0/CPU0:Sep 4 00:17:20.669 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: EEM policy vrr_remediation_script.tcl has started
RP/0/RP0/CPU0:Sep 4 00:17:27.742 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script for node RR251 - unregister_detection procedure started------
RP/0/RP0/CPU0:Sep 4 00:17:31.610 UTC: config[67666]: %MGBL-CONFIG-6-DB_COMMIT : Configuration committed by user 'eem-user'. Use 'show configuration commit changes 1000000887' to view the changes.
RP/0/RP0/CPU0:Sep 4 00:17:31.928 UTC: config[67666]: %MGBL-SYS-5-CONFIG_I : Configured from console by console on vty101 (0.0.0.0)
RP/0/RP0/CPU0:Sep 4 00:17:32.411 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script on backup vRR RR253 - unregister_detection procedure completed------
RP/0/RP0/CPU0:Sep 4 00:17:32.411 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script for node RR251 on backup vRR - load_commit_file procedure started------
RP/0/RP0/CPU0:Sep 4 00:17:36.418 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: vrr_remediation_script load_config procedure SUCCESSFUL to load disk0:/eem/configs/RR251_bgp_cfg
RP/0/RP0/CPU0:Sep 4 00:17:36.419 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: EEM policy vrr_remediation_script - Config load opeartion completed SUCCESSFULLY with config for prior active node RR251
RP/0/RP0/CPU0:Sep 4 00:17:36.419 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script for node RR251 on backup vRR RR253 - load_config procedure completed------
RP/0/RP0/CPU0:Sep 4 00:17:37.710 UTC: config[67726]: %MGBL-CONFIG-6-DB_COMMIT : Configuration committed by user 'eem-user'. Use 'show configuration commit changes 1000000888' to view the changes.
RP/0/RP0/CPU0:Sep 4 00:17:42.830 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: EEM policy vrr_remediation_script - Config commit opeartion completed SUCCESSFULLY, with config for prior active node RR251
RP/0/RP0/CPU0:Sep 4 00:17:42.830 UTC: bgp[1060]: %ROUTING-BGP-5-ADJCHANGE : neighbor 12.122.249.213 Up (VRF: default) (AS: 13979)
RP/0/RP0/CPU0:Sep 4 00:17:42.964 UTC: bgp[1060]: %ROUTING-BGP-5-ADJCHANGE : neighbor 12.122.249.248 Up (VRF: default) (AS: 13979)
RP/0/RP0/CPU0:Sep 4 00:17:43.048 UTC: config[67726]: %MGBL-SYS-5-CONFIG_I : Configured from console by console on vty102 (0.0.0.0)
RP/0/RP0/CPU0:Sep 4 00:17:43.132 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script for node RR251 on backup vRR RR253 - commit_config procedure completed------

## Slide 58: Remediation Script Logs (on vRRb becoming active)
RP/0/RP0/CPU0:Sep 4 00:18:13.157 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_syslog_remediation script for backup vRR - ping_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:18:15.875 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: EEM Remediation Script - CBB Loopback Ping check for 12.122.0.7 SUCCESSFUL, script will continue with the checks.
RP/0/RP0/CPU0:Sep 4 00:18:18.679 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: EEM Remediation Script - CBB Loopback Ping check for 12.122.0.4 SUCCESSFUL, script will continue with the checks.
RP/0/RP0/CPU0:Sep 4 00:18:18.681 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script on backup vRR RR253 - ping_check procedure completed------
RP/0/RP0/CPU0:Sep 4 00:18:18.682 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_syslog_remediation script for backup vRR - bgp_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:18:21.268 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_syslog_remediation script for backup vRR - bgp_check procedure total number of vpnv4 sessions { 11} ------
RP/0/RP0/CPU0:Sep 4 00:18:23.805 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_syslog_remediation script for backup vRR - bgp_check procedure total number of vpnv4 sessions Active { 1} ------
RP/0/RP0/CPU0:Sep 4 00:18:26.485 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_syslog_remediation script for backup vRR - bgp_check procedure total number of vpnv4 sessions Idle { 3} ------
RP/0/RP0/CPU0:Sep 4 00:18:26.486 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_syslog_remediation script for backup vRR - bgp_check procedure found 4 down vpnv4 sessions ------
RP/0/RP0/CPU0:Sep 4 00:18:26.490 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: EEM Remediation Script - BGP VPNv4 Session check down percentage 0.363636363636 < 0.5, script will contine with the checks.
RP/0/RP0/CPU0:Sep 4 00:18:26.491 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script on backup vRR RR253 - bgp_check procedure completed------
RP/0/RP0/CPU0:Sep 4 00:18:26.492 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script on backup vRR RR253 - final check completed------
RP/0/RP0/CPU0:Sep 4 00:18:26.493 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: Sending Email Alert - EEM vRR Remediation Script for node RR251 to gtamilse@cisco.com
RP/0/RP0/CPU0:Sep 4 00:18:26.625 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script for node RR251 - register_recovery procedure started------
RP/0/RP0/CPU0:Sep 4 00:18:31.319 UTC: eem_policy_dir[326]: %HA-HA_EM-6-FMPD_POLICY_REG_SUCC : fh_reg_unreg_policy: Policy 'vrr_recovery_script.tcl' registered successfully, by user eem-user, with persist time 3600 and type 2
RP/0/RP0/CPU0:Sep 4 00:18:32.428 UTC: config[68092]: %MGBL-CONFIG-6-DB_COMMIT : Configuration committed by user 'eem-user'. Use 'show configuration commit changes 1000000889' to view the changes.
RP/0/RP0/CPU0:Sep 4 00:18:32.810 UTC: config[68092]: %MGBL-SYS-5-CONFIG_I : Configured from console by console on vty103 (0.0.0.0)
RP/0/RP0/CPU0:Sep 4 00:18:33.289 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script on backup vRR RR253 - register_recovery procedure completed successfully------
RP/0/RP0/CPU0:Sep 4 00:18:33.290 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script for node RR251 completed!!------

## Slide 59: Remediation Script Logs (on vRRb becoming active)
RP/0/RP0/CPU0:Sep 4 00:18:26.493 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: Sending Email Alert - EEM vRR Remediation Script for node RR251 to gtamilse@cisco.com
RP/0/RP0/CPU0:Sep 4 00:18:26.625 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script for node RR251 - register_recovery procedure started------
RP/0/RP0/CPU0:Sep 4 00:18:31.319 UTC: eem_policy_dir[326]: %HA-HA_EM-6-FMPD_POLICY_REG_SUCC : fh_reg_unreg_policy: Policy 'vrr_recovery_script.tcl' registered successfully, by user eem-user, with persist time 3600 and type 2
RP/0/RP0/CPU0:Sep 4 00:18:32.428 UTC: config[68092]: %MGBL-CONFIG-6-DB_COMMIT : Configuration committed by user 'eem-user'. Use 'show configuration commit changes 1000000889' to view the changes.
RP/0/RP0/CPU0:Sep 4 00:18:32.810 UTC: config[68092]: %MGBL-SYS-5-CONFIG_I : Configured from console by console on vty103 (0.0.0.0)
RP/0/RP0/CPU0:Sep 4 00:18:33.289 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script on backup vRR RR253 - register_recovery procedure completed successfully------
RP/0/RP0/CPU0:Sep 4 00:18:33.290 UTC: tclsh[67562]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_remediation_script.tcl: ------EEM policy vrr_remediation_script for node RR251 completed!!------

## Slide 60: Recovery Script Logs (on vRRb becoming backup)
RP/0/RP0/CPU0:Sep 4 00:18:54.536 UTC: bgp[1060]: %ROUTING-BGP-5-ADJCHANGE : neighbor 12.122.250.251 Up (VRF: default) (AS: 13979)
RP/0/RP0/CPU0:Sep 4 00:18:54.718 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: EEM policy vrr_recovery_script.tcl has started
RP/0/RP0/CPU0:Sep 4 00:18:56.689 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup node RR253 - extract_data procedure SUCCESSFUL.------
RP/0/RP0/CPU0:Sep 4 00:19:01.695 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - ping_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:19:04.394 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: EEM policy vrr_recovery_script PING to IP 9.3.249.251 of RR251 successful, script will exit and send alert.
RP/0/RP0/CPU0:Sep 4 00:19:04.394 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - ping_check procedure for Old Active vRR's MGMT IP 9.3.249.251 SUCCESSFUL------
RP/0/RP0/CPU0:Sep 4 00:19:04.398 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - ping_check procedure for Old Active vRR's MGMT IP completed------
RP/0/RP0/CPU0:Sep 4 00:19:04.399 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script Backup file (vrr-recovery-active) created for RR251 on backup node RR253------
RP/0/RP0/CPU0:Sep 4 00:19:04.400 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - unregister_remediation procedure started------
RP/0/RP0/CPU0:Sep 4 00:19:08.332 UTC: config[68308]: %MGBL-CONFIG-6-DB_COMMIT : Configuration committed by user 'eem-user'. Use 'show configuration commit changes 1000000890' to view the changes.
RP/0/RP0/CPU0:Sep 4 00:19:08.711 UTC: config[68308]: %MGBL-SYS-5-CONFIG_I : Configured from console by console on vty101 (0.0.0.0)
RP/0/RP0/CPU0:Sep 4 00:19:09.192 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - unregister_remediation procedure completed - Successful------
RP/0/RP0/CPU0:Sep 4 00:19:09.193 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: Sending Email Alert - EEM vRR Recovery Script for node RR251 to gtamilse@cisco.com

## Slide 61: Recovery Script Logs (on vRRb becoming backup)
RP/0/RP0/CPU0:Sep 4 00:19:14.309 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 on backup vRR - load_commit_file procedure started------
RP/0/RP0/CPU0:Sep 4 00:19:18.610 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: vrr_recovery_script load_config procedure SUCCESSFUL to load disk0:/eem/configs/recovery_cleanup_cfg
RP/0/RP0/CPU0:Sep 4 00:19:18.611 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: EEM policy vrr_recovery_script - Config load operation completed SUCCESSFULLY with config for prior active node RR251
RP/0/RP0/CPU0:Sep 4 00:19:18.611 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 on backup vRR RR253 - load_config procedure completed------
RP/0/RP0/CPU0:Sep 4 00:19:20.022 UTC: config[68372]: %MGBL-CONFIG-6-DB_COMMIT : Configuration committed by user 'eem-user'. Use 'show configuration commit changes 1000000891' to view the changes.
RP/0/RP0/CPU0:Sep 4 00:19:20.974 UTC: bgp[1060]: %ROUTING-BGP-5-ADJCHANGE : neighbor 12.122.249.248 Down - Address family removed (CEASE notification sent - configuration change) (VRF: default) (AS: 13979)
RP/0/RP0/CPU0:Sep 4 00:19:20.985 UTC: bgp[1060]: %ROUTING-BGP-5-ADJCHANGE : neighbor 12.122.0.73 Down - Neighbor moved to a new cluster (VRF: default) (AS: 13979)
RP/0/RP0/CPU0:Sep 4 00:19:25.121 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: EEM policy vrr_recovery_script - Config commit operation completed SUCCESSFULLY, with config for prior active node RR251
RP/0/RP0/CPU0:Sep 4 00:19:25.338 UTC: config[68372]: %MGBL-SYS-5-CONFIG_I : Configured from console by console on vty102 (0.0.0.0)
RP/0/RP0/CPU0:Sep 4 00:19:25.424 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 on backup vRR RR253 - commit_config procedure completed------
RP/0/RP0/CPU0:Sep 4 00:19:55.459 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - loopback 0 route_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:19:57.937 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: EEM Recovery Script - RIB Route check for 12.122.249.251 of RR251 show route is PRESENT, script will continue with the checks.
RP/0/RP0/CPU0:Sep 4 00:19:57.938 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - route_check procedure for Old Active vRR's Loopback0 IP 12.122.249.251 SUCCESSFUL------
RP/0/RP0/CPU0:Sep 4 00:19:57.938 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - route_check procedure for Old Active vRR's Loopback0 IP completed------
RP/0/RP0/CPU0:Sep 4 00:19:57.939 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - ping_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:20:00.689 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: EEM policy vrr_recovery_script PING to IP 12.122.249.251 of RR251 successful, script will exit and send alert.
RP/0/RP0/CPU0:Sep 4 00:20:00.689 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - ping_check procedure for Old Active vRR's Loopback0 IP 12.122.249.251 SUCCESSFUL------
RP/0/RP0/CPU0:Sep 4 00:20:00.691 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - ping_check procedure for Old Active vRR's Loopback0 IP completed------
RP/0/RP0/CPU0:Sep 4 00:20:00.691 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - remove_files procedure started------
RP/0/RP0/CPU0:Sep 4 00:20:02.391 UTC: run_cmd[68601]: %INFRA-INFRA_MSG-5-RUN_LOGIN : User eem-user logged into shell from vty103
RP/0/RP0/CPU0:Sep 4 00:20:03.338 UTC: run_cmd[68601]: %INFRA-INFRA_MSG-5-RUN_LOGOUT : User eem-user logged out of shell from vty103
RP/0/RP0/CPU0:Sep 4 00:20:03.367 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - remove_files procedure completed - Successful------
RP/0/RP0/CPU0:Sep 4 00:20:03.367 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - register_detection procedure started------
RP/0/RP0/CPU0:Sep 4 00:20:07.988 UTC: eem_policy_dir[326]: %HA-HA_EM-6-FMPD_POLICY_REG_SUCC : fh_reg_unreg_policy: Policy 'vrr_detection_script.tcl' registered successfully, by user eem-user, with persist time 3600 and type 2
RP/0/RP0/CPU0:Sep 4 00:20:08.929 UTC: config[68916]: %MGBL-CONFIG-6-DB_COMMIT : Configuration committed by user 'eem-user'. Use 'show configuration commit changes 1000000892' to view the changes.
RP/0/RP0/CPU0:Sep 4 00:20:09.296 UTC: config[68916]: %MGBL-SYS-5-CONFIG_I : Configured from console by console on vty104 (0.0.0.0)
RP/0/RP0/CPU0:Sep 4 00:20:09.682 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - register_detection procedure completed - Successful------
RP/0/RP0/CPU0:Sep 4 00:20:09.683 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_remediation_script for node RR251 - Final Check completed------
RP/0/RP0/CPU0:Sep 4 00:20:09.685 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: Sending Email Alert - EEM vRR Recovery Script for node RR251 to gtamilse@cisco.com
RP/0/RP0/CPU0:Sep 4 00:20:09.810 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on node RR251 completed!!------
RP/0/RP0/CPU0:Sep 4 00:20:14.816 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - Recovery script will unregister itself
RP/0/RP0/CPU0:Sep 4 00:20:14.818 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - unregister_recovery procedure started------
RP/0/RP0/CPU0:Sep 4 00:20:19.701 UTC: sysdb_mc[409]: %SYSDB-SYSDB-2-CLEARED_CONFIG_INCONSISTENCY : The running config and persistent configuration maybe out of sync (most likely due to a config session closed before it is completed). The system automatically executed 'clear configuration inconsistency' successfully and rectified it (however, there is no commit id so rollback won't work).
RP/0/RP0/CPU0:RR253-VRR#

## Slide 62: Recovery Script Logs (on vRRb becoming backup)
RP/0/RP0/CPU0:Sep 4 00:19:57.939 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - ping_check procedure started------
RP/0/RP0/CPU0:Sep 4 00:20:00.689 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: EEM policy vrr_recovery_script PING to IP 12.122.249.251 of RR251 successful, script will exit and send alert.
RP/0/RP0/CPU0:Sep 4 00:20:00.689 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - ping_check procedure for Old Active vRR's Loopback0 IP 12.122.249.251 SUCCESSFUL------
RP/0/RP0/CPU0:Sep 4 00:20:00.691 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - ping_check procedure for Old Active vRR's Loopback0 IP completed------
RP/0/RP0/CPU0:Sep 4 00:20:00.691 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - remove_files procedure started------
RP/0/RP0/CPU0:Sep 4 00:20:02.391 UTC: run_cmd[68601]: %INFRA-INFRA_MSG-5-RUN_LOGIN : User eem-user logged into shell from vty103
RP/0/RP0/CPU0:Sep 4 00:20:03.338 UTC: run_cmd[68601]: %INFRA-INFRA_MSG-5-RUN_LOGOUT : User eem-user logged out of shell from vty103
RP/0/RP0/CPU0:Sep 4 00:20:03.367 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - remove_files procedure completed - Successful------
RP/0/RP0/CPU0:Sep 4 00:20:03.367 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - register_detection procedure started------
RP/0/RP0/CPU0:Sep 4 00:20:07.988 UTC: eem_policy_dir[326]: %HA-HA_EM-6-FMPD_POLICY_REG_SUCC : fh_reg_unreg_policy: Policy 'vrr_detection_script.tcl' registered successfully, by user eem-user, with persist time 3600 and type 2
RP/0/RP0/CPU0:Sep 4 00:20:08.929 UTC: config[68916]: %MGBL-CONFIG-6-DB_COMMIT : Configuration committed by user 'eem-user'. Use 'show configuration commit changes 1000000892' to view the changes.
RP/0/RP0/CPU0:Sep 4 00:20:09.296 UTC: config[68916]: %MGBL-SYS-5-CONFIG_I : Configured from console by console on vty104 (0.0.0.0)
RP/0/RP0/CPU0:Sep 4 00:20:09.682 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - register_detection procedure completed - Successful------
RP/0/RP0/CPU0:Sep 4 00:20:09.683 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_remediation_script for node RR251 - Final Check completed------
RP/0/RP0/CPU0:Sep 4 00:20:09.685 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: Sending Email Alert - EEM vRR Recovery Script for node RR251 to gtamilse@cisco.com
RP/0/RP0/CPU0:Sep 4 00:20:09.810 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on node RR251 completed!!------
RP/0/RP0/CPU0:Sep 4 00:20:14.816 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - Recovery script will unregister itself
RP/0/RP0/CPU0:Sep 4 00:20:14.818 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - unregister_recovery procedure started------
RP/0/RP0/CPU0:Sep 4 00:20:19.701 UTC: sysdb_mc[409]: %SYSDB-SYSDB-2-CLEARED_CONFIG_INCONSISTENCY : The running config and persistent configuration maybe out of sync (most likely due to a config session closed before it is completed). The system automatically executed 'clear configuration inconsistency' successfully and rectified it (however, there is no commit id so rollback won't work).
RP/0/RP0/CPU0:RR253-VRR#

## Slide 63: Recovery Script Logs (on vRRb becoming backup)
RP/0/RP0/CPU0:Sep 4 00:20:09.683 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_remediation_script for node RR251 - Final Check completed------
RP/0/RP0/CPU0:Sep 4 00:20:09.685 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: Sending Email Alert - EEM vRR Recovery Script for node RR251 to gtamilse@cisco.com
RP/0/RP0/CPU0:Sep 4 00:20:09.810 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on node RR251 completed!!------
RP/0/RP0/CPU0:Sep 4 00:20:14.816 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script on backup vRR RR253 - Recovery script will unregister itself
RP/0/RP0/CPU0:Sep 4 00:20:14.818 UTC: tclsh[68174]: %HA-HA_EEM-6-ACTION_SYSLOG_LOG_INFO : vrr_recovery_script.tcl: ------EEM policy vrr_recovery_script for node RR251 - unregister_recovery procedure started------
RP/0/RP0/CPU0:Sep 4 00:20:19.701 UTC: sysdb_mc[409]: %SYSDB-SYSDB-2-CLEARED_CONFIG_INCONSISTENCY : The running config and persistent configuration maybe out of sync (most likely due to a config session closed before it is completed). The system automatically executed 'clear configuration inconsistency' successfully and rectified it (however, there is no commit id so rollback won't work).
RP/0/RP0/CPU0:RR253-VRR#